## Slide 1: FPGA Adaptive Beamforming with HDL Coder and Zynq RFSoC

## Slide 2: Agenda
Introduction: Motivation and Challenges
  Applications: Radar, Comms and Wireless
  Hardware FPGA challenges
Theory and Implementation
  Linear algebra
  QR Decomposition
  Matrix Divide
Zynq RFSoC and HDL Coder Implementation
  MATLAB MVDR reference code
  HDL Coder implementation
  Hardware Prototyping – live demo

## Slide 3: Adaptive Beamforming
Algorithm chooses optimal weights based on receive data statistics
Improve SNR by automatically placing nulls at interference angles
+
Adaptive Algorithm
w1
w2
w3
w4
Interferer
Signal of interest

## Slide 4: Applications: Radar
Increase angular resolution
Suppress interference

## Slide 5: Applications: 5G
Increase number of simultaneous users
Improve throughput and coverage

## Slide 6: FPGA Implementation Challenges
Fixed-Point Math
Performance vs Area tradeoffs
Data Rate vs Clock Rate
Project Timeline

## Slide 7: Agenda
Introduction: Motivation and Challenges
  Applications: Radar, Comms and Wireless
  Hardware FPGA challenges
Theory and Implementation
  Linear algebra
  QR Decomposition
  Matrix Divide
Zynq RFSoC and HDL Coder Implementation
  MATLAB MVDR reference code
  HDL Coder implementation
  Hardware Prototyping – live demo

## Slide 19: Agenda
Introduction: Motivation and Challenges
  Applications: Radar, Comms and Wireless
  Hardware FPGA challenges
Theory and Implementation
  Linear algebra
  QR Decomposition
  Matrix Divide
Zynq RFSoC and HDL Coder Implementation
  MATLAB MVDR reference code
  HDL Coder implementation
  Hardware Prototyping – live demo

## Slide 20: HDL Implementation Workflow
MATLAB Reference
Hardware Architecture
Fixed-point Implementation
HDL Code Generation and Optimization
Simulink
HDL Coder
Fixed Point Designer
HDL Verification and Targeting
MATLAB
Integrated Verification

## Slide 21: MATLAB MVDR reference code
function Y = mvdr_beamform(X, sv)
% form covariance matrix
Ecx = X.'*conj(X);
% compute weight vector
wp = Ecx\sv;
% normalize response
w = wp/(sv'*wp);
% form output beam
Y = X*conj(w);
end
100+ hours of design time saved!

## Slide 22: HDL Implementation of MVDR Beamforming

## Slide 23: HDL Implementation of MVDR Beamforming

## Slide 24: Form Covariance Matrix
For Each subsystem
  Process elements independently
  Concatenate results into outputs
% form covariance matrix
Ecx = X.'*conj(X);

## Slide 25: Moving Average
Use HDL Implementation properties to map large delays to Block RAM

## Slide 26: Compute Weight Vector
Use Systolic CORDIC Complex Matrix Solver
% compute weight vector
wp = Ecx\sv;
100+ hours of design time saved!
See the example model:
>> fi_complex_mldivide_systolic_array_model

## Slide 27: Normalize Response
Perform divide using reciprocal and multiply
Fixed-point CORDIC reciprocal “just works”
% normalize response
w = wp/(sv'*wp);

## Slide 28: Implementation Results
Device: xczu28dr (ZCU111)
Maximum frequency: 335.9 MHz
Resource utilization:
Resource | Utilization | (%)
LUT | 63K | 14.8
LUTRAM | 1.3K | 0.6
FF | 45K | 5.3
BRAM | 6 | 0.6
URAM | 8 | 10.0
DSP | 150 | 3.5
Xilinx ZCU111 RFSoC Eval Board
MATLAB
Simulink
Ethernet

## Slide 29: Resources to Get Started and Speed Adoption
Getting started:
  MATLAB Onramp
  Simulink Onramp
  HDL pulse detector self-guided tutorial and videos
Proof-of-concept guided evaluations
  FREE support via weekly WebEx meetings using custom sample designs
  MathWorks coaches customers on “how to fish” through weekly WebEx sessions
Training & consulting services
  HDL code generation, FPGA signal processing & Zynq programming training courses
  Consulting service on deep technical coaching, custom design / hardware and more
Notes: Please edit this to include other callouts specific to your event!

## Slide 30: Q&A